## Slide 1
Brain-Body Co-Design for Embodied Agents: An Introduction and Recent Advances
Speaker：Yuxing Wang (Tsinghua SIGS)
Mail: wyx20@tsinghua.org.cn

## Slide 2
Traditional View
Recent Achievements of Embodied Intelligence
Huang, Wenlong, et al. "Voxposer: Composable 3d value maps for robotic manipulation with language models." arXiv preprint arXiv:2307.05973 (2023).
https://www.tesla.com/en_hk/AI
“Brain”（LLM+VLM）+ “body”(Robotic Arm)
Tesla Bot

## Slide 3
Traditional View
Smith, Linda, and Michael Gasser. "The development of embodied cognition: Six lessons from babies." Artificial life 11.1-2 (2005): 13-29.
Traditional View of EI
Human intelligence is a result of the program running on our brains
Mind is essentially independent of the body
What is Embodied Intelligence?
RL loop

## Slide 4
Smith, Linda, and Michael Gasser. "The development of embodied cognition: Six lessons from babies." Artificial life 11.1-2 (2005): 13-29.
Brain, Body and Environment
Howard, David, Jack Collins, and Nicole Robinson. "Taking shape: A perspective on the future of embodied cognition and a new generation of evolutionary robotics." IOP Conference Series: Materials Science and Engineering. Vol. 1261. No. 1. IOP Publishing, 2022.

## Slide 5
Traditional View
Between Informational Computation and Morphological Computation
Hoffmann, Matej, and Vincent C. Müller. "Simple or complex bodies? Trade-offs in exploiting body morphology for control." Representation and reality in humans, other living organisms and intelligent machines (2017): 335-345.
More embodied systems require physical interactions as driving forces of behaviors
Rely on physical self-organization at the minimum level

## Slide 6
structure and joint-specific
Target: Finding the optimal agent morphology and its control policy for solving a given task
The agent’s skeletal structure and joint-specific attributes (e.g., bone length, size, and motor strength)
Problem Formulation of Brain-Body Co-Design
Where
Original MDP
: Control Policy

## Slide 7
structure and joint-specific
How do we solve Brain-Body Co-Design problem?
Representation of body and brain
Optimization Methods
Modeling of system dynamic

## Slide 8
structure and joint-specific
Representation of body and brain
Optimization Methods
Modeling of system dynamic
Ma, Pingchuan, et al. "Diffaqua: A differentiable computational design pipeline for soft underwater swimmers with shape interpolation." ACM Transactions on Graphics (TOG) 40.4 (2021): 1-14.
Xu, Jie, et al. "Accelerated policy learning with parallel differentiable simulation." arXiv preprint arXiv:2204.07137 (2022).
What if the simulator (physical dynamics) is differentiable?
Concatenating these steps allows us to propagate gradients through an entire trajectory

## Slide 9
structure and joint-specific
Representation of body and brain
Optimization Methods
Modeling of system dynamic
Ma, Pingchuan, et al. "Diffaqua: A differentiable computational design pipeline for soft underwater swimmers with shape interpolation." ACM Transactions on Graphics (TOG) 40.4 (2021): 1-14.
Xu, Jie, et al. "Accelerated policy learning with parallel differentiable simulation." arXiv preprint arXiv:2204.07137 (2022).
What if the simulator (physical dynamics) is non-differentiable?
How about the model-free methods?

## Slide 10
structure and joint-specific
Ha D. Reinforcement learning for improving agent design[J]. Artificial life, 2019, 25(4): 352-365.
Cheney N, Bongard J, SunSpiral V, et al. Scalable co-optimization of morphology and control in embodied machines[J]. Journal of The Royal Society Interface, 2018, 15(143): 20170937.
Yuan Y, Song Y, Luo Z, et al. Transform2Act: Learning a Transform-and-Control Policy for Efficient Agent Design[J]. arXiv preprint arXiv:2110.03659, 2021.
Indirect encoding（CPPN）
Representation of body and brain
Optimization Methods
Modeling of system dynamic
Direct encoding
Indirect encoding（GNN）
Implicit Function/Signed Distance Function Linear Interpolation/Wasserstein Barycenter ……
Parameterization of the design space

## Slide 11
Spiking neural network
Ha D. Reinforcement learning for improving agent design[J]. Artificial life, 2019, 25(4): 352-365.
Cheney N, Bongard J, SunSpiral V, et al. Scalable co-optimization of morphology and control in embodied machines[J]. Journal of The Royal Society Interface, 2018, 15(143): 20170937.
Yuan Y, Song Y, Luo Z, et al. Transform2Act: Learning a Transform-and-Control Policy for Efficient Agent Design[J]. arXiv preprint arXiv:2110.03659, 2021.
Representation of body and brain
Optimization Methods
Modeling of system dynamic
Closed-loop (Neural Networks)
Open-loop
Parameterization of the state-action space
Spiking NNs
FNNs
Graph NNs
Transformers
Central Pattern Generator (CPG) controller
Sine/Square/Cosine-wave controller

## Slide 12
Learning from scratch in the target design space
Representation of body and brain
Optimization Methods
Modeling of system dynamic
The separate training procedures significantly hinder the experience of design and control to be shared across different robots
Learning from scratch in the target design space with expensive fitness evaluation
Bi-level optimization loop
The unified design-and-control MDP
Control policy
Gradient-based RL training (PPO etc.)
Design policy
Environment
…
…
reward=0
reward=environmental reward
Design
Control
Reinforcement learning based
Evolutionary Computation based
Difficulties

## Slide 13
Traditional View
Representation of body and brain
Optimization Methods
Modeling of system dynamic
CuCo: Learning to design and control from easy to difficult
ICLR 2023 Poster
PreCo: Enhancing Generalization in Co-Design via Brain-Body Pre-Training
CoRL 2023 Oral
Wang, Yuxing, et al. "Curriculum-based co-design of morphology and control of voxel-based soft robots." The Eleventh International Conference on Learning Representations. 2022.
Wang, Yuxing, et al. "PreCo: Enhancing Generalization in Co-Design of Modular Soft Robots via Brain-Body Pre-Training." Conference on Robot Learning. PMLR, 2023.

## Slide 14
Traditional View
Next: Co-Design in the Real World
Voxcraft
Nygaard, Tønnes F., et al. "Real-world evolution adapts robot morphology and control to hardware limitations." Proceedings of the Genetic and Evolutionary Computation Conference. 2018.
Zhenishbek Zhakypov, Mohsen Falahi, Manan Shah, and Jamie Paik, The design and control of the multi-modal locomotion origami robot, Tribot , IEEE/RSJ International Conference on Intelligent Robots and Systems, IROS
Real-World Evolution
Revolve2 Platform
More robotic agents

## Slide 15
Thank you！
For more information